Some Slides from:
Introduction to Sequential Circuits
Some Slides from:
- U.C. Berkeley,
- Alan Mishchenko,
- Mike Miller,
- Gaetano Borriello

---
State Minimization
State Minimization
Goal : identify and remove redundant states
(states which can not be observed from the
FSM I/O behavior)
Why : 1. Reduce number of latches
      - assign minimum-length encoding
      - only as the logarithm of the number
      of states
2. Increase the number of unassigned states
codes
      - heuristic to improve state-assignment
      and logic-optimization

---
Algorithmic State Minimization
Algorithmic State Minimization
- Goal – identify and combine states that have equivalent behavior
- Equivalent States:
  - Same output
  - For all input combinations, states transition to same or equivalent states
Algorithm Sketch
  1. Place all states in one set
  2. Initially partition set based on output behavior
  3. Successively partition resulting subsets based on next state transitions
  4. Repeat (3) until no further partitioning is required
    - states left in the same set are equivalent
  Polynomial time procedure

---
State Minimization Definition
State Minimization Definition
Completely-specified state machine
  - two states are equivalent if outputs are
  identical for all input combinations
  Next states are equivalent for all input
  combinations
  - equivalence of states is an equivalence relation which partitions the states into disjoint equivalence classes
Incompletely specified state machines

---
Classical State Minimization
Classical State Minimization
1. Partition states based on input output values
asserted in the state
2. Define the partitions so that all states in a partition transition into the same next-state partition (under corresponding inputs)

---
Basic Principle of State Minimization for Completely Specified Machines
Basic Principle of State Minimization for Completely Specified Machines
Procedure (fast) for lazy students
- Any two states of Moore Machine that have the same output and transit to the same states under the same input symbols are equivalent and can be combined
- This step is repeated until no more equivalent states exist
States SZ and SZ are equivalent and are combined to one state by pointing all arows that go to SY to state SZ and removing SY with its all arrows
SA
X
X
X
X
SC
SY
SZ

---
Procedure (fast) for lazy students (for Mealy machines)
- Any two states of Mealy Machine that have the same output for the same input symbol and transit to the same states under the same input symbols are equivalent and can be combined
- This step is repeated until no more equivalent states exist
Z
Z
Z
Z
SZ
X
Z
SC
X
SA
Z
States SZ and SZ are equivalent and are combined to one state by pointing all arows that go to SY to state SZ and removing SY with its all arrows
SA
X
X
X
X
SC
SY
SZ

---
Classical State Minimization Algorithm
Classical State Minimization Algorithm
Only for Completely specified Machines
1. Partition the set of internal states based on input output values asserted in the state
2. Define the partitions so that all states in a partition transition into the same next-state partition (under corresponding inputs)

---
Example (FSM in Kiss format)
Example (FSM in Kiss format)
G has other input-output response than other states
Ex :
0 A B 0
1 A C 0
0 B D 0 (A,B,C,D,E,F,H) (G)
1 B E 0
0 C F 0 (A,B,C,E,F,H)(G)(D)
1 C A 0
0 D H 0 (A,C,E)(G)(D)(B,F)(H)
1 D G 0
0 E B 0
1 E C 0
0 F D 0
1 F E 0
0 G F 1
1 G A 0
0 H H 0
1 H A 0
D has other input-output response than other states because it goes to G which is known to be non-equivalent state-goes to red and blue groups
B and F go to D
States A, C and E can be combined to one state
States B and F can be combined to one state
Please check this using triangular table
You can also marke each new group with a new symbol and check transitions to thus marked groups

---
Example of partition based minimization
Example of partition based minimization
Ex :
0 A B 0
1 A C 0
0 B D 0 (A,B,C,D,E,F,H)(G)
1 B E 0
0 C F 0 (A,B,C,E,F,H)(G)(D)
1 C A 0
0 D H 0 (A,C,E,H)(G)(D)(B,F)
1 D G 0
0 E B 0 (A,C,E)(G)(D)(B,F)(H)
1 E C 0
0 F D 0
1 F E 0
0 G F 1
1 G A 0
0 H H 0
1 H A 0

---
State Minimization Example
State Minimization Example
Sequence Detector for 010 or 110
Input	Next State	Output
Sequence	Present State	X=0	X=1	X=0	X=1
Reset	S0	S1	S2	0	0
0	S1	S3	S4	0	0
1	S2	S5	S6	0	0
00	S3	S0	S0	0	0
01	S4	S0	S0	1	0
10	S5	S0	S0	0	0
11	S6	S0	S0	1	0
S0
S3
S2
S1
S5
S6
S4
1/0
0/0
1/0
1/0
0/1
0/0
1/0
0/0
1/0
0/0
1/0
0/1
1/0
0/0

---
Method of Successive Partitions
Method of Successive Partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S3 S5 ) ( S1 S2 ) ( S4 S6 )
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )
S1 is equivalent to S2
S3 is equivalent to S5
S4 is equivalent to S6
Input	Next State	Output
Sequence	Present State	X=0	X=1	X=0	X=1
Reset	S0	S1	S2	0	0
0	S1	S3	S4	0	0
1	S2	S5	S6	0	0
00	S3	S0	S0	0	0
01	S4	S0	S0	1	0
10	S5	S0	S0	0	0
11	S6	S0	S0	1	0

---
Minimized FSM
Minimized FSM
State minimized sequence detector for 010 or 110
Input	Next State	Output
Sequence	Present State	X=0	X=1	X=0	X=1
Reset	S0	S1'	S1'	0	0
0 + 1	S1'	S3'	S4'	0	0
X0	S3'	S0	S0	0	0
X1	S4'	S0	S0	1	0
S0
S1’
S3’
S4’
X/0
1/0
1/0
0/1
0/0
X/0

---
More Complex State Minimization
More Complex State Minimization
Multiple input example
inputs here
symbolic state
transition table
present	next state output
 state	00	01	10	11
   S0	S0	S1	S2	S3	1
   S1	S0	S3	S1	S4	0
   S2	S1	S3	S2	S4	1
   S3	S1	S0	S4	S5	0
   S4	S0	S1	S2	S5	1
   S5	S1	S4	S0	S5	0
10
01
11
00
00
01
11
10
10
01
11
00
10
00
11
00
11
10
01
10
11
01
00
S0
[1]
S2
[1]
S4
[1]
S1
[0]
S3
[0]
S5
[0]
01

---
Implication Chart Method
  - Cross out incompatible states based on outputs
  - Then cross out more cells if indexed chart entries are already crossed out
S0-S1
S1-S3
S2-S2
S3-S4
S0-S0
S1-S1
S2-S2
S3-S5
S0-S1
S3-S0
S1-S4
S4-S5
S0-S1
S3-S4
S1-S0
S4-S5
S1-S0
S3-S1
S2-S2
S4-S5
S4-S0
S5-S5
S1-S1
S0-S4
minimized state table
(S0==S4) (S3==S5)
present	next state output
 state	00	01	10	11
   S0'	S0'	S1	S2	S3'	1
   S1	S0'	S3'	S1	S3'	0
   S2	S1	S3'	S2	S0'	1
   S3'	S1	S0'	S0'	S3'	0
S1
S2
S3
S4
S5
S0
S1
S2
S3
S4

---
Minimizing Incompletely Specified FSMs
Minimizing Incompletely Specified FSMs
- Equivalence of states is transitive when machine is fully specified
- But its not transitive when don't cares are present
  e.g.,	state	output
  S0	– 0	S1 is compatible with both S0 and S2
  S1	1 –	but S0 and S2 are incompatible
  S2	– 1
- No polynomial time algorithm exists for determining best grouping of states into equivalent sets that will yield the smallest number of final states

---
Minimizing States May Not Yield Best Circuit
Minimizing States May Not Yield Best Circuit
Example: edge detector - outputs 1 when last two input changes from 0 to 1
Q1+ = X (Q1 xor Q0)
Q0+ = X Q1’ Q0’
X	Q1	Q0	Q1+	Q0+
0	0	0	0	0
0	0	1	0	0
0	1	1	0	0
1	0	0	0	1
1	0	1	1	1
1	1	1	1	1
–	1	0	0	0
00
[0]
11
[0]
01
[1]
X’
X’
X’
X
X
X

---
"Ad hoc" solution - not minimal but cheap and fast
00
[0]
10
[0]
01
[1]
X’
X
X’
X
X
X
11
[0]
X’
X’